## Slide 1: Pixel detector MX-10
Author: Jakub Indrei
Supervisors: Vladimír Vícha, Kiril Gikal
University Center of JINR

## Slide 2: Aim of the project
Aim of this project was to learn to work with a modern type of detector of ionizing radiation, namely MX-10 pixel detector.
Next aim was to meassure emitters with different types of ionizing radiation without any shielding and with different types of shielding, mainly aluminium.
Last aim was to take an air sample in room and to meassure the radioactivity of radon decay elements.

## Slide 3: Aplications of pixel detectors

## Slide 4: MX-10 description
Silicon chip
  Area: 14x14 mm, 256x256 = 65 536 pixels
  Area each pixel: 55x55 μm
  Thickness: 300 μm
Function
  Visualisation of traces of ionizing radiation,
  particle resolution, particle counting,
  energy meassurement
Principe of detection and processing signal
Silicon chip
Set of Jablotron MX-10 Edukit
MX-10, pixel detector
Scheme of detector layout

## Slide 5: Pixelman
Heavy blob: E = 6 473 keV, 36 pixels
Heavy track: E = 1929 keV, 42 pixels
Straght track: E = 2688 keV, 136 pixels
Pixelman´s window from meassurement in flight
Examples of resolution of detected particles

## Slide 6: Results
4000 frames: 239Pu, 226Ra; 2000 frames: 22Na, 90Sr
exp. time = 0.001 s
239Pu
47744 detected particles (43440 alpha)
226Ra
79098 detected particles (45332 alpha)
60Co
23143 detected particles (15108 beta)
22Na
31222 detected particles (25249 beta)

## Slide 7: Characterization of sources
RN | A (kBq) | T1/2 | E (keV) … a, b | E (keV) … g | X-ray (keV)
239Pu | 38.720 | 24110 y | a 5157(70.79%), 5144(17.14%), 5106(11.87%) |  | 11-20, 95, 98, 110-111, 114-115
226Ra | 38.800 | 1600 y | a 4784(94.038%), 4601(5.95%) | 186(3.555%) | 10-17, 81, 84, 94-95
60Co | 112.8 | 5.27 y | b- max.317(99.98%) avg.95,6 | 1173 (99.85%), 1332(99.98%) | 7-8
137Cs | 102.6 | 30.05 y | b- max.514(94.36%) avg.174, max. 1176(5.64%) avg.416 | 662 (84.99%) | 31-32, 36-37
22Na | 109.1 | 2.6 y | b+ max.546(90.30%) avg.216 | 1275(99.94%), 511 anihilation | Pod 1keV

## Slide 8: Shielding x-rays radiation 137Cs by aluminium
Chart: Shielding x-rays radiation Cs-137 by Al
Chart: Dependence x-ray on aluminium thickness
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8
 | 2292 | 1620 | 1408 | 1069 | 801 | 622 | 520 | 442 | 332 | 271 | 192 | 134 | 163 | 78 | 58 | 37

## Slide 9: Results – meassurement air sample in room
80. frame: 64 particles
Time of air sampling = 5 min;
Number of frames = 469;
Time of 1 frame = 30 s;
Chart: Dependence detected particles on the time
2. frame: 113 particles
150. frame 38 particles
468. frame 6 particles

## Slide 10: Thank you for your attention!